## Slide 1
PulseCam
Shri Ramswaroop Memorial University
Uttar Pradesh
Heart rate and pulse waveform from a webcam face video, live
Aryan Singh
Roll no. 202310101150038
Ruchi Singh
Roll no. 202310101150025
Ananya Dwivedi
Roll no. 202310101150039
B.Tech CS (DS + AI) | Group 71, 72
Research prototype. Not a medical device, never diagnostic.
Notes: Introduce the project and say clearly that this is a research prototype, not a medical device.

## Slide 2
Why measure heart rate from a face?
Today
Finger clips, smartwatches and chest straps all need contact and a device on the body.
Our goal
One normal webcam, 30 seconds, nothing worn. Heart rate and a pulse waveform on screen.
The gap
Public rPPG data has few darker skin tones, so we test fairness across Monk skin-tone bands (E4).
Notes: Contact sensors versus a webcam. The fairness gap motivates the skin-tone experiment E4.

## Slide 3
How rPPG works
1
Heartbeat
Each beat pushes blood into the face skin.
2
Colour change
Skin colour shifts by a tiny amount, mostly in green. Eyes cannot see it, a camera can.
3
Frequency
Filter 0.7 to 3.0 Hz, then take the strongest frequency with an FFT.
HR = 60 x f
f is the peak frequency in Hz
1.8 Hz
= 108 beats per minute
Notes: Explain simply: heartbeat, tiny colour change, filter and FFT peak gives the heart rate.

## Slide 4
The pipeline
Video
30 fps webcam
Face + skin
MediaPipe box, crop 72x72
Model
POS or TS-CAN
Bandpass
0.7 to 3.0 Hz
FFT peak
HR = 60 x f
Live demo
10 s rolling buffer (300 frames), a new estimate every second, the median of the last 5 is shown. A 'Hold still' warning appears on motion, darkness or a weak signal.
Notes: Walk left to right. TS-CAN outputs the derivative of the pulse, so we integrate it before the filter.

## Slide 5
Three kinds of model
Classical
GREEN, ICA, CHROM, POS
Hand-made colour maths. No training needed. CHROM and POS are the strong ones.
TS-CAN
Deep network
Temporal-shift attention CNN from rPPG-Toolbox. We use its released PURE and SCAMPS weights.
Fine-tuning
Tried on UBFC
Person-wise split, 30 train, 6 valid, 6 test. Result: 1.60 vs 1.58 BPM, no real gain, so the released model stays.
Notes: Fine-tuning was person-wise so nobody appears in both train and test. We report that it gave no gain.

## Slide 6
Data and experiments
Item | What | Status
E1 | Classical baselines vs deep model on UBFC-rPPG (42 people) | Done
E2 | PURE and SCAMPS weights tested on UBFC | Done
Fine-tune | UBFC person-wise split, released weights kept | Done, no gain
E3, E4 | Robustness per condition, skin-tone bands | Needs volunteers
E5 | Live demo vs a reference device | Needs hardware
Scored on 490 ten-second windows per method against the heart rate of the ground-truth pulse.
Notes: Be upfront that E3 to E5 need people and hardware and were not done.

## Slide 7
E1 and E2: error by method
Chart: Mean absolute error per 10 s window, BPM (lower is better)
| TS-CAN (PURE) | CHROM | POS | ICA | TS-CAN (SCAMPS) | GREEN
Window MAE (BPM) | 1.8 | 2 | 4.5 | 6.73 | 12.83 | 19.38
1.80 vs 2.00
TS-CAN (PURE) vs CHROM, BPM per window
Tied per video
Median 0.72 BPM for both. The deep model only narrowly beats the best classical method.
Notes: 42 UBFC subjects, 490 windows per method. SCAMPS weights transfer poorly; we checked five ways and it is not a scoring bug.

## Slide 8
The live demo app
1
Go live
30 s webcam measurement
2
Upload video
Analyse a recorded clip
3
Results
E1 and E2 tables, Bland-Altman plots
4
Status
Project checklist
Python, Starlette and a browser page. Works offline, no cloud, nothing leaves the laptop.
Notes: Screenshot of the running app on localhost. Live webcam run with a person is still untested.

## Slide 9
Results tab in the app
Headline numbers, error bars per method and a Bland-Altman plot for every model, read straight from the results tables.
How to read it honestly
TS-CAN edges out CHROM, but by a small margin.
Per video the two are exactly tied.
UBFC fine-tuning gave no gain.
No result here says anything medical.
Notes: Screenshot of the Results tab. Stress that the margin over CHROM is small.

## Slide 10
Limits and next steps
Not done yet
No volunteer recordings or consent forms
No reference device, so no E3, E4 or E5
Live webcam test with a person pending
Next
Record volunteers with signed consent
Score against a finger-clip or watch
Fine-tune on own recordings, person-wise
A research prototype, never a medical device. Faces and consent forms are never committed; people are P01, P02 and so on.
Notes: Close with limitations and ethics, then thank the audience.